## Slide 1: IE 563 Experimental Design in Engineering
Dr. Erin Gerber, P.E.
Department of Industrial Engineering
University of Louisville

## Slide 2: References
Montgomery, Design and Analysis of Experiments, 8th Edition, John Wiley & Sons, New York, 2013.
Box, Hunter, Hunter, Statistics for Experimenters: Design, Innovation, and Discovery, 2nd edition, Wiley-Interscience, 2005.
Kuehl, Design of Experiments: Statistical Principles of Research Design and Analysis, 2nd edition, Cengage Learning, 1999.
Oehlert, A First Course in Design and Analysis of Experiments, W.H. Freeman and Company, 2000.
Berger and Maurer, Experimental Design with Applications in Management, Engineering and the Sciences, Duxbury, 2001.
Based on slides by Dr. Gail DePuy

## Slide 3: Minitab Software
We will be using Minitab software throughout this course.
Download free Minitab from UofL IT
Minitab can also be accessed from Citrix Receiver

## Slide 4: Chapter 1 Introduction to Designed Experiments

## Slide 5: What is Experimental Design?
An experiment is a test, or a series of tests, in which purposeful changes are made to the controllable input variables of a process or system so that we may observe and identify the reasons for changes in the output response.
Make purposeful changes to factors (i.e. independent or controllable input variables) to determine affect on the response (i.e. dependent variables or output).
Determine which factors significantly affect the response.
Determine how significant factors affect the response.

## Slide 6: Random Experiments
System
Input
(materials)
Output (response)
Controlled Variables
(factors)
Noise (random) Variables
An experiment that can result in different outcomes, even though it is repeated in the same manner every time, is a called a random experiment.
System output affected by known sources of variation and random variation.
Examples: baseball hitting, car braking distance, concrete strength.
Controllable variables?
And random variation!

## Slide 7: Why use Experimental Design?
How to learn about and control complex systems?
  Mathematical/Mechanistic Model
  Empirical Model: Experimentation
    Examples: Car brake distance, Concrete strength
How to mathematically model the system and its variation?
  Why study variation? When we incorporate variation into our thinking and analysis, we can make informed judgments that are not invalidated by the variation
How to use model to draw conclusions or make predictions?

## Slide 8: Objectives of the Experiment
Determine which factors (independent variables) most affect the response (dependent variable).
Determine where to set the influential factors so the response is near a desired nominal value.
Determine where to set factors so that variation in response is minimized .

## Slide 9
Some of the factors affect the location of the response variable (average or mean value).
Some affect the response dispersion (standard deviation).
Some affect both response location and dispersion.
The rest have no influence on the response variables.
One objective of the data analysis is to determine which of these factors affect the response average, which affect the standard deviation, which affect both, and which have no affect.

## Slide 10
Factor A affects the average response
Factor B affects the response standard deviation
A1
A2
B1
B2
response
response
Distribution of responses from repeated experiments
A1 : factor A, level (setting) 1
A2 : factor A, level (setting) 2

## Slide 11
Factor C affects the response average and standard deviation
Factor D has no effect on response average or standard deviation
C1
C2
D1 = D2
response
response

## Slide 12: Design of Experiments (DOE)
Classical design of experiments is a formal methodology wherein purposeful changes in the factors are made with the aim to observe the resulting changes in the response variables.
Vital few factors are determined from the analysis of resulting data.
With the vital few factors identified, mathematical models for predicting the response variable and its standard deviation can be developed.
These models will be used to determine the values of the factors which will provide the best response average and the lowest possible standard deviation of the response variable(s).

## Slide 13: Potential Results of Designed Experiment
Evaluation of materials, design alternatives, setting component & system tolerances, etc.
Improve performance of existing processes
Achieve product & process robustness
Improve reliability and performance of products
Reduce time to design/develop new products & processes

## Slide 14: Need for Statistical Analysis Cake Baking Example
Goal: Bake a fluffy cake.
Response: Cake height (measured in inches)
Potential Factors:
  # eggs
  Amount of flour
  Oven temperature
  Shape of baking pan
  Brand of flour
  Type of oven

## Slide 15: Cake Baking Example (cont.)
Not all factors will have a significant effect on cake height.
How to determine which factors are significant?
How to predict cake height for given factor levels?
How to choose factor levels (settings) to achieve desired cake height?

## Slide 16: Cake Baking Example (cont.)
Could(?) develop and analyze equations for all chemical reactions in cake baking
OR Could perform an experiment
Simple example….
  Determine if # eggs (factor) affects cake height (response).
  Bake cakes at several factor levels (2 eggs, 3 eggs, 4 eggs) and compare cake heights.

## Slide 17: Cake Baking Example (cont.)
Bake 5 cakes at each of the 3 factor levels.
Do you expect all cakes baked with 3 eggs to be exactly the same height? Suppose all other factors held constant.
No! Why?
RANDOM VARIATION

## Slide 18: Cake Baking Example (cont.)
Experiment 2
Experiment 1
Does # eggs affect cake height?
Does it matter whether I use 2, 3 or 4 eggs?
Is a 0.74” difference in average cake height enough to conclude #eggs does affect cake height?

## Slide 19: Cake Baking Example (cont.)
In both experiments the average cake heights were the same.
However the spread or variance of the cake height is larger in experiment 2 (i.e. more random variation).
Our conclusion (does # eggs affect cake height?) depends on both
  Comparison of average responses at each factor level
  Comparison of variance between avg. level responses to random variation (variance of responses within each factor level)

## Slide 20: Cake Baking Example (cont.)
If the variance between avg. level responses is much larger than the random variation, then factor significantly affects response.
How large is ‘much larger’?
Do statistical test called Analysis of Variance (ANOVA).
Once significant factors identified, predictive model can be built

## Slide 21: Cake Baking Example (cont.)
Use Regression Analysis to build a predictive model.
Cake ht = 1.7 + 0.4*(# eggs)
Note: This was a simple example (only one factor; # eggs). Your experiment could have many factors.
Cake ht = 0.3 + 0.1*(# eggs)+0.2*(cups of flour) – 0.05*(oven temp)

## Slide 22: 3 Basic Principles of DOE
Replication – repeating entire experiment
  Cake baking experiment had 5 replicates
  2 important properties of replication
    Estimation of random error
    Precision of estimates
Randomization – both allocation of experimental material and order in which experimental runs are conducted should be randomized
  Average out uncontrolled factors
Blocking – increase precision of random error estimate by eliminating known source of variation

## Slide 23: DOE Steps
Problem statement
Choose response(s)
Choose factors and levels
Perform experiment
Data analysis
Conclusions and recommendations

## Slide 24: Step 1. Problem Statement
Clearly define goals of experiment
Involve many departments
  Engineering
  Management
  Marketing
  Manufacturing
  Quality Control
  Customer service

## Slide 25: Step 2: Choose Response
Response must be measurable
Response must be measured on continuous scale to use Linear Regression
  No binary responses (yes/no, go/no go, etc.)
  No categorical responses (small/medium/large, 5 point scales, etc.)
  Can use Logistic Regression for non-continuous responses

## Slide 26: Step 3: Choose Factors and Levels
Requires process knowledge.
Mathematically no limit on number of factors, HOWEVER smaller number of factors will keep experiment simple and aid interpretation of results.
Must have a finite number of factor levels for ANOVA.
Can have an ‘infinite’ number of factor levels for regression analysis.
Many experiments use 2 levels of each factor
  Simplifies data collection
  Simplifies analysis

## Slide 27: Step 4: Perform Experiment
Choose number of replicates (number of repeated observations at same combination of factor levels) to obtain a desired degree of confidence.
More replicates = more confidence
More replicates = more time = more $
DOE software packages or Taguchi methods can be used to choose sample size

## Slide 28: Step 4: Perform Experiment (cont.)
Use randomized run order to ensure independent observations and to ‘average out’ uncontrolled variables
  Learning curve
  Fatigue
  Machine wear
Be careful – sloppy execution can significantly affect results

## Slide 29: Step 5: Data Analysis
ANOVA
  ANOVA Table
  Main effects and interaction plots
  Residual analysis – check ANOVA assumptions
Regression analysis
  Regression equation
  R2 value – evaluate model fit
  Residual analysis
Use statistical software
  Minitab - Design Ease
  SAS - R
  SPSS

## Slide 30: Step 6: Conclusions and Recommendations
Try to keep models simple to aid interpretation
Experimentation should be iterative
  major mistake to develop one large experiment
  generally expend only 25% of resources on the 1st set of experiments

## Slide 31: Step 6: Conclusions and Recommendations (cont.)
Statistical vs practical significance
  Just because a factor is statistically significant does not necessarily mean it has practical value
  e.g. Cake baking experiment
    Factor: brand of flour
    2 Levels: cheap ($1/cup), expensive ($4/cup)
    Expensive flour found to produce cakes, on average, 0.2” taller than cheap flour
    0.2” may be a statistically significant difference, but 0.2” not of practical consequence given dramatic cost difference

## Slide 32: Four Eras in the History of DOE
The agricultural origins, 1918 – 1940s
  R. A. Fisher & his co-workers
  Profound impact on agricultural science
  Factorial designs, ANOVA
The first industrial era, 1951 – late 1970s
  Box & Wilson, response surfaces
  Applications in the chemical & process industries
The second industrial era, late 1970s – 1990
  Quality improvement initiatives in many companies
  Taguchi and robust parameter design, process robustness
The modern era, beginning circa 1990

## Slide 33: Chapter 2 Statistics Review

## Slide 34: Statistic Review
Numerical Summaries of Data
  Descriptive Statistics
    Mean, Variance, Median
  Graphical presentation of data
    Histogram, Probability Plot
Sampling Distributions
Simple experiments
  Confidence Intervals
  Hypothesis Testing

## Slide 35: Statistics
The field of statistics deals with the collection, presentation, analysis, and use of data to:
  Make decisions
  Solve problems
  Design products and processes
Statistical techniques are useful for describing and understanding variability.
Statistics gives us a framework for describing this variability and for learning about potential sources of variability.
  Known source of variation
  Random variation

## Slide 36: Numerical Summaries of Data
Conduct experimentation and collect data
How to characterize data so we can use it to draw conclusions and make decisions?
In most analyses, we work with a sample of observations selected from a population we wish to study
  Population – the entire collection of objects or outcomes about which information is sought
  Sample – subset of the population measured by the experimenter
  Suppose we are interested in numerically describing the length of adult feet (to make socks)
    Population = all adults in the world? All adults in USA?
    Sample 1 = all students at UofL
    Sample 2 = all students in this class

## Slide 37: Numerical Summaries of Data
Figure Relationship between a population and a sample.

## Slide 38: Descriptive Statistics
A statistic is a function of the observations in a random sample.
Some common statistics
Suppose the sample has n observations denoted x1, x2, …, xn
  Sample Mean
  Sample Variance
  Sample Standard Deviation
Note: Mean can be negative, but s2 and s cannot be negative

## Slide 39: Descriptive Statistics
A parameter is a function of the observations in a population.
Some common parameters
Suppose the population has N observations denoted x1, x2, …, xN
  Population Mean
  Population Variance
  Population Standard Deviation
Analogous to mean, variance, and standard deviation of probability distribution

## Slide 40: Descriptive Statistics
The sample variance is calculated with the quantity n-1 called the “degrees of freedom”.
Origin of the term:
  There are n deviations from x-bar in the sample.
  The sum of the deviations is zero. (Balance point)
  n-1 of the observations can be freely determined, but the nth observation is fixed to maintain the zero sum.
The true population variance is based on data deviations from the true population mean, μ.
The sample variance is based on the data deviations from x-bar, not μ. X-bar is an estimator of μ; close but not the same. So the n-1 divisor is used to compensate for the error in using x-bar to estimate μ.

## Slide 41: Descriptive Statistics
Sample Variance is Sum of Squares divided by degrees of freedom (df), often called Mean Square
So, a mean square is a measure of dispersion or variance

## Slide 42: Descriptive Statistics
Use Mean and Variance to summarize probability distribution of rv
Mean is measure of center of distribution
  Mean = balance point of loading
Variance is measure of spread or dispersion of distribution
The sample mean as a balance point
8 Observations:
12.6 12.9 13.4 12.3 13.6 13.5 12.6 13.1
12 13 14

## Slide 43: Descriptive Statistics
Sample variance measures variability through deviations
12 13 14

## Slide 44: Descriptive Statistics
The median is a measure of central tendency that divides the data into two equal parts, half below the median and half above.
Sort data from smallest to largest observation
If n is odd, then the median is the rounddown(n/2) +1 observation
If n is even, then the median is halfway between the n/2 and (n/2)+1 observations.
12.3 12.6 12.6 12.9 13.1 13.4 13.4 13.6
Median = 13.0 cm

## Slide 45: Descriptive Statistics
Figure 6-11 Histograms for symmetric and skewed distributions.
Relationship between mean and median helps determine if distribution is symmetric or skewed

## Slide 46: Descriptive Statistics in Minitab
Enter data in single column

## Slide 47: Descriptive Statistics in Minitab
Stat
  Basic Statistics
    Display Descriptive Statistics
        Enter Column
        Choose Statistics

## Slide 48: Descriptive Statistics in Minitab
Descriptive Statistics: C1
Total
Variable Count Mean StDev Median Range
C1 8 13.000 0.478 13.000 1.300

## Slide 49: Descriptive Statistics
Mean and variance DO NOT uniquely describe a distribution.
  Different distributions can have the same mean and variance
However they are simple, useful summaries of the probability distribution

## Slide 50: Histograms
A frequency distribution or histogram helps us visualize the general shape of the distribution
  To construct a frequency distribution, divide the range of the data into intervals of equal width, which are usually called class intervals, cells, or bins. Above each bin, draw a rectangle whose height is equal to the frequency or relative frequency.

## Slide 51: Histograms in Minitab
Enter data in single column
Graph
  Histogram
    Simple
Enter column

## Slide 52: Histograms in Minitab

## Slide 53: Probability Plots
How do we know what distribution is a good fit to our data?
  Normal? Uniform? Exponential?
Probability plotting is a graphical method for determining whether sample data conform to a hypothesized distribution based on a subjective visual examination of the data.
In the past, probability plotting used special graph paper that has been designed for the hypothesized distribution.
  Vertical axis scaled for distribution such that plotted data will appear as a straight line if data well fit by distribution
We’ll use Minitab

## Slide 54: Probability Plots in Minitab
Enter data in single column
Graph
  Probability Plot (NOT Probability Distribution Plot)
    Enter column
    Choose distribution
      (default: Normal Distr)

## Slide 55: Probability Plots in Minitab
Straight fitted distribution line (middle blue line) a good fit?
High P-Value (close to 1) and Low AD Stat (close to 0) indicate good fit
  P-value is probability this distribution is a good fit

## Slide 56: Probability Plots in Minitab
Straight fitted distribution line good fit?
Low P-Value and High AD Stat indicate bad fit

## Slide 57: Foot Length Sample
Back to our sock problem……
Interested in length of adult feet
Measured foot length (in cm) of 28 students in Prob & Stat course (i.e. sample size = n = 28)
25.38 | 29.38 | 27.95 | 27.34 | 25.51 | 25.25 | 28.25
24.95 | 24.43 | 23.66 | 23.04 | 27.69 | 24.64 | 25.30
26.90 | 25.45 | 26.51 | 29.49 | 26.17 | 26.61 | 29.59
24.75 | 26.77 | 25.03 | 26.45 | 27.16 | 28.96 | 24.41

## Slide 58: Foot Length Sample
Descriptive Statistics: foot length
Variable Mean StDev Minimum Median Maximum
foot length 26.322 1.786 23.040 26.310 29.590

## Slide 59: Foot Length Sample

## Slide 60: How to use Sample
Statistical inference is concerned with making decisions about a population based on the information contained in a random sample from that population
However there could be lots of different samples
  Foot length example
How to generalize the info from our sample to make decision about population?
Parameter: property of unknown probability distribution or population
  Mean, μ, or variance, σ2
Statistic: property of a sample. A statistic is any function of the observations in a random sample.
  Sample mean, x, or sample variance, s2
  Statistics are known. We use statistics to estimate unknown parameters

## Slide 61: Statistical Inference
Example: Suppose we are interested in the average length of an adult’s foot
Measure everyone’s foot? Calculate μ? 
Take random sample of 28 people
Calculate sample mean, x = 26.32 cm
Estimate the population average foot length. Estimate μ.
x is a point estimate for μ.
HOWEVER, different samples will have different x

## Slide 62: Sampling Distributions
Foot length example
Go to 100 different UofL classes and measure feet of 28 students (i.e. 100 samples, each of size 28)

## Slide 63: Sampling Distributions
Foot length example
100 samples, each n=28
Calculate sample mean, x, and sample variance, s2, for each sample

## Slide 64: Sampling Distributions
Foot length example
Distribution of sample means and sample variances
s2 ~ Chi-squared distr
x ~ Normal distr
x ~ Student t distr

## Slide 65: Sampling Distributions
Sampling distribution for sample mean when large sample (n≥40) → Normal distribution
Sampling distribution for sample mean when small sample (n<40) → Student-t distribution
Sampling distribution for sample variance → Chi-squared distribution
Sampling distribution of the ratio of two sample variances → F Distribution
How to use sample statistic and sampling distribution to make inference about population parameter?
  Confidence Intervals
  Hypothesis Testing

## Slide 66: Confidence Intervals
How to estimate a population parameter using sample statistics?
  Estimate mean length of adult foot. Measure 28 students and find X = 26.322 cm. Is this a good estimate for μ?
  Do we believe μ EXACTLY equals 26.322 cm (μ=X)?
  What if we measure the foot lengths of a different sample of 28 students?
Rather than estimate μ with a single value (called point estimate) let’s develop range or interval of values (called interval estimate) we think contains true value of μ.
  Now rather than saying μ = 26.322 cm, we say 25.77 ≤ μ ≤ 26.87 cm

## Slide 67: Confidence Intervals
A confidence interval for an unknown population parameter θ (e.g. μ, σ2) is an interval that contains a set of plausible or believable values of the parameter.
  Confidence interval: lower limit ≤ θ ≤ upper limit (L ≤ θ ≤ U)
  Example CI on population mean μ: 25.77 ≤ μ ≤ 26.87 cm
Definition of 100(1-α)% CI on θ: P(L ≤ θ ≤ U) = 1-α
  How likely the CI is to contain the unknown population parameter θ is determined by the confidence level, 1-α
confidence level is 1-α
where 0 ≤ α ≤ 1

## Slide 68: Confidence Intervals
Common 100(1-α)% CI:
    99% CI: P(L ≤ θ ≤ U) = 0.99 → 1-α = 0.99 → α = 0.01
    95% CI: P(L ≤ θ ≤ U) = 0.95 → 1-α = 0.95 → α = 0.05
    90% CI: P(L ≤ θ ≤ U) = 0.90 → 1-α = 0.90 → α = 0.10
Why not use 100% CI? Or 99.9999% CI ?
The width of a CI is a measure of the precision of estimation.
The wider the CI, the more confident we are that the interval actually contains the true value of θ.
      as confidence level (i.e. 1-α) ↑, CI width ↑
However, the wider the CI the less information we have about the true value of θ
Ideal situation: a relatively narrow interval with high confidence.
  This is possible when sample size is large and/or variance is small.

## Slide 69: Confidence Intervals
      We take one sample and calculate CI. How do we know if our CI really contains θ?
        We do NOT know. But we know likelihood it does (i.e. 1-α)
How to calculate upper and lower CI limits?
  Take sample and calculate sample statistics
  Using the sampling distribution of the appropriate sample statistic, choose 100(1-α)% CI such that P(L ≤ θ ≤ U) = 1-α
e.g. Sampling distribution for sample mean when large sample (n≥40) is Normal distribution
Choose L and U such that the 100(1-α)% CI for all sample mean in this range will contain μ i.e. P(L ≤ μ ≤ U) = 1-α

## Slide 70: CI on the Mean, μ, for Large Sample
100(1-α)% Confidence Interval on μ
CI centered around sample mean, X
CI width (upper limit – lower limit) is a function of:
  Confidence level, 1-α
    As confidence level ↑, CI width ↑
  Sample size (i.e. # observations)
      As sample size↑, CI width ↓
  Variance of data (as measured by S2)
      As variance ↑, CI width ↑
Upper limit
Lower limit
where Zα/2 is the upper 100(α/2) percentage point of N(0,1)

## Slide 71: Simple Experiments: CI
Single population
CI on mean, µ, large sample (n≥40)
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound
Believable µ=µ0?
Yes, if µ0 contained in CI
Be careful interpreting one-sided CI
Statement is believable if ALL values in CI satisfy statement
If CI completely contained in statement, then statement is believable
where Zα/2 is the upper 100(α/2) percentage point of N(0,1)

## Slide 72: Simple Experiments: CI
Single population
CI on mean, µ, small sample (n<40)
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound
Remember: Student t Distribution is sampling distribution of the sample mean, when sample size is small (n<40) and underlying distribution is Normal (or close to Normal)

## Slide 73: Simple Experiments: CI
Single population
CI on variance, σ2
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound
Remember: Chi squared Distribution is sampling distribution of the sample variance, when underlying distribution is Normal (or close to Normal)
Believable σ2=σ02?
Yes, if σ02 contained in CI

## Slide 74: Simple Experiments: CI
Two populations
CI on means, comparing µ1 and µ2, large sample (n≥40)
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound
Believable µ1=µ2? Yes, if 0 contained in CI
where Zα/2 is the upper 100(α/2) percentage point of N(0,1)

## Slide 75: Simple Experiments: CI
Two populations
CI on means, comparing µ1 and µ2, small sample (n < 40) AND population variances assumed to be equal (i.e. σ21 = σ22 )
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound

## Slide 76: Simple Experiments: CI
Two populations
Test on means, comparing µ1 and µ2, small sample (n<40) AND population variances assumed to be unequal (i.e. σ21 ≠ σ22 )
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound

## Slide 77: Simple Experiments: CI
Two populations
Test on variances, comparing σ12 and σ22
100(1-α)% two-sided CI
100(1-α)% upper-confidence bound
100(1-α)% lower-confidence bound
Note: F 1-α,u,v = 1/ F α,v,u
Remember: F Distribution is sampling distribution of the ratio of two sample variance, when underlying distributions are Normal (or close to Normal)
Believable σ12=σ22? Yes, if 1 contained in CI

## Slide 78: Simple Experiments: CI
How to know which CI to use?
Single population or two populations?
What is parameter of interest? µ or σ2?
  If interested in mean, µ, of single population, is sample large? Or is sample small?
  If interested in comparing means, µ1 vs µ2, of two populations with unknown variances (i.e. small samples), are population variances assumed to be the same (i.e. σ21 = σ22 )? Or different (i.e. σ21 ≠ σ22 )?
One-sided or Two-sided test?
Be careful interpreting one-sided CI
Statement is believable if ALL values in CI satisfy statement
If CI completely contained in statement, then statement is believable

## Slide 79: Simple Experiments: CI
A textile manufacturer wants to find a 95% confidence interval on the mean breaking strength of a fiber.
The manufacturer collects a sample of 50 fibers and finds the sample mean to be 215 psi and the sample standard deviation to be 100 psi.
α = 0.05 Xbar = 215 S = 100 n = 50
95% CI on µ
Believable that µ = 200psi? µ =150 psi?
From N(0,1) table, Z0.025 = 1.96

## Slide 80: Simple Experiments: CI
Confidence Intervals in Minitab
Enter data in column(s) or can enter summarized data
For our previous example….
>Stat
>Basic Statistics
>1-sample Z
Default is 95% two-sided CI
‘Options’ to change confidence level and one-sided CI

## Slide 81: Simple Experiments: CI
One-Sample Z
The assumed standard deviation = 100
N Mean SE Mean 95% CI
50 215.0 14.1 (187.3, 242.7)
Believable that µ = 200psi? µ =150 psi?

## Slide 82: CI and Hypothesis Testing
Both CI and Hypothesis testing are used to make a statistical inference
  Use sample statistic to ‘guess’ population parameter
In CI we formed an interval around sample statistic and used the interval to answer questions
  Believable that μ=12? Believable that σ<3.2?
In hypothesis testing we are making a statement about the population parameter then using the sample statistic to decide whether the statement is believable or not

## Slide 83: Hypothesis Testing
Now we’ll learn how to accept or reject a statement or hypothesis about an unknown population parameter (μ, σ2)
Make statement, called Null Hypothesis, H0, about population parameter,θ
  Examples: H0: μ = 27.0 H0: σ ≤ 3.27
Actually make 2 contradictory statements about population parameter,θ
    Null Hypothesis, H0 versus Alternative Hypothesis, H1
    Two-sided test: H0: θ = θ0 versus H1: θ ≠ θ0
    One-sided tests: H0: θ ≤ θ0 versus H1: θ > θ0
    H0: θ ≥ θ0 versus H1: θ < θ0
A Statistical Hypothesis is a statement about a population parameter

## Slide 84: Hypothesis Testing
Then use sample statistic (e.g. X, S2) to decide if H0 is believable
Example: H0: μ = 27.0 cm
      H1: μ ≠ 27.0 cm
    If sample mean, X = 26.8 cm, I would believe H0: μ = 27.0 cm
      If sample mean, X = 21.0 cm, I would NOT believe H0: μ = 27.0 cm
      I would believe H1: μ ≠ 27.0 cm
      Assume null hypothesis, H0, is true unless sample provides overwhelming evidence H0 is not true
Make statement, H0, about unknown population mean, μ
Use sample mean to decide if statement, H0, is believable

## Slide 85: Hypothesis Testing
  How close does sample mean, X, need to be to 27.0 cm for me to believe H0: μ = 27.0 cm?
  How far away from 27 cm does the sample mean, X, need to be for me to believe H1: μ ≠ 27.0 cm?
How to decide to accept or reject H0 based on sample?
      Always in terms of accepting/rejecting H0 , NOT H1
  When we accept H0 we are saying H0 is plausible or believable. However accepting H0 does not prove H0 to be true.
Depends on:
  Variance, σ2
  Sample size, n
  Significance level, α
Same factors that determine CI width

## Slide 86: Hypothesis Testing
  We either Accept or Reject H0 based on our sample statistic
  Our decision to accept or reject H0 will either be right or wrong.
    We’ll never know for certain whether we’re right or wrong (because we do not know population parameter), but we can find the probability we’re wrong
    Two ways we could be wrong:
      Reject H0 when H0 is true (type I error)
      Accept H0 when H0 is false (type II error)

## Slide 87: Hypothesis Testing
Probability of Type I error = α Reject H0 when H0 is true
Probability of Type II error = β Accept H0 when H0 is false
Power, 1-β, is the probability of correctly rejecting a false null hypothesis.
We often compare statistical tests by comparing their power
 | H0 True | H0 False
Accept H0 | correct | Type II error
Reject H0 | Type I error | correct
  α called significance level
  1-β called power of the hypothesis test

## Slide 88: Hypothesis Testing
How to decide to accept or reject H0? How to choose critical values?
  State H0 and H1
  Choose significance level, α
  Take sample and calculate sample statistics
  Use the sampling distribution of the appropriate sample statistic to determine critical values and therefore whether to accept or reject H0
  e.g. Use Normal distribution to find critical values for population mean, μ, when n≥40
The 100(1-α)% sample means closest to μ0 are acceptance region
where Zα/2 is the upper 100(α/2) percentage point of N(0,1)

## Slide 89: Hypothesis Testing
μ0
1-α
  Choose critical values based on specified probability of type 1 error, α
Critical values
Accept H0
Reject H0
Reject H0
Common values of α
  α = 0.05
  α = 0.01
  α = 0.10
Why not choose α=0?
i.e. no type I error
  As α gets smaller, acceptance region gets bigger
  All sample mean will support H0: μ = μ0
  No meaningful info about μ

## Slide 90: Hypothesis Testing
The “strongest” inference is available when the null hypothesis is rejected.
  Sample provides overwhelming evidence H0 is not believable
This point is important when an experimenter decides what should be the null hypothesis and what should be the alternative hypothesis for one-sided problems.
In order to “prove” or establish a statement (say μ > μ0) it is necessary to make it the alternative hypothesis (H1).
For one-sided hypothesis test, make H1 the statement you are evaluating

## Slide 91: Simple Experiments: Hypothesis Testing
Single population
Test on mean, µ, large sample (n≥40)
Null hypothesis: H0: μ=μ0
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: μ ≠ μ0 |Z0| > Z α/2
H1: μ > μ0 Z0 > Z α
H1: μ < μ0 Z0 < −Z α

## Slide 92: Simple Experiments: Hypothesis Testing
Single population
Test on mean, µ, small sample (n<40)
Null hypothesis: H0: μ=μ0
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: μ ≠ μ0 |T0| > t α/2,n-1
H1: μ > μ0 T0 > t α,n-1
H1: μ < μ0 T0 < −t α, n-1

## Slide 93: Simple Experiments: Hypothesis Testing
Single population
Test on variance, σ2
Null hypothesis: H0: σ2 = σ02
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: σ2 ≠ σ02 X02 > X2α/2,n-1 or X02 < X21-(α/2),n-1
H1: σ2 > σ02 X02 > X2α,n-1
H1: σ2 < σ02 X02 < X21-α,n-1

## Slide 94: Simple Experiments: Hypothesis Testing
Two populations
Test on means, µ1 and µ2, large sample (n≥40)
Null hypothesis: H0: μ1=μ2
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: μ1 ≠ μ2 |Z0| > Z α/2
H1: μ1 > μ2 Z0 > Z α
H1: μ1 < μ2 Z0 < −Z α

## Slide 95: Simple Experiments: Hypothesis Testing
Two populations
Test on means, µ1 and µ2, small sample (n < 40) AND population variances assumed to be equal (i.e. σ21 = σ22 )
Null hypothesis: H0: μ1=μ2
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: μ1 ≠ μ2 |t0| > t α/2,n1+n2-2
H1: μ1 > μ2 t0 > t α,n1+n2-2
H1: μ1 < μ2 t0 < -t α,n1+n2-2
where

## Slide 96: Simple Experiments: Hypothesis Testing
Two populations
Test on means, µ1 and µ2, small sample (n < 40) AND population variances assumed to be unequal (i.e. σ21 ≠ σ22 )
Null hypothesis: H0: μ1=μ2
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: μ1 ≠ μ2 |t0| > t α/2,v
H1: μ1 > μ2 t0 > t α,v
H1: μ1 < μ2 t0 < -t α,v
where

## Slide 97: Simple Experiments: Hypothesis Testing
Two populations
Test on variances, comparing σ12 and σ22
Null hypothesis: H0: σ12 = σ22
Test Alternative
Statistic Hypothesis H0 Rejection Criteria
H1: σ12 ≠ σ22 F0 > F α/2, n1-1,n2-1 OR F0 < F 1-(α/2), n1-1,n2-1
H1: σ12 > σ22 F0 > F α,n1-1,n2-1
H1: σ12 < σ22 F0 < F 1-α,n1-1,n2-1

## Slide 98: Simple Experiments: Hypothesis Testing
How to know which test statistic to use?
Single population or two populations?
What is parameter of interest? µ or σ2?
  If interested in mean, µ, of single population, is sample large? Or is sample small?
  If interested in comparing means, µ1 vs µ2, of two populations with unknown variances (i.e. small samples), are population variances assumed to be the same (i.e. σ21 = σ22 )? Or different (i.e. σ21 ≠ σ22 )?
One-sided or Two-sided test?

## Slide 99: Simple Experiments: Hypothesis Testing
Example
Two catalysts are being analyzed to determine how they affect the mean yield of a chemical process.
Specifically, catalyst 1 is currently in use, but catalyst 2 is acceptable. Since catalyst 2 is cheaper, it should be adopted, providing it does not change the process yield.
A test is run using each catalyst and the results follow. Is there any difference between the mean yields of catalysts 1 and 2?

## Slide 100: Simple Experiments: Hypothesis Testing
H0: µ1=µ2
H1: µ1≠µ2

## Slide 101: Simple Experiments: Hypothesis Testing
Which test statistic to use?
Comparing 2 populations
Test on means
Small samples → variance unknown
Variances assumed to be equal? or unequal?
  Can do hypothesis test to first determine whether variances equal. Then choose proper test statistic to compare means.
t test statistic

## Slide 102: Simple Experiments: Hypothesis Testing
First determine if population variances equal or unequal.
H0: σ21 = σ22
H1: σ21 ≠ σ22
F0 = 2.392/2.982 = 0.6432
Critical region values for α = 0.05:
  F0.025,7,7 = 4.99
  F0.975,7,7 = 0.20
Since F0 = 0.6432 < 4.99 AND F0 = 0.6432 > 0.20 we DO NOT reject H0. We believe the variances are equal.
Note: F 1-α,u,v = 1/ F α,v,u

## Slide 103: Simple Experiments: Hypothesis Testing
Now we know which t test statistic to use to test the means
H0: µ1 = µ2
H1: µ1 ≠ µ2
Critical region values for α=0.05
  t 0.025,14 = 2.145
Since |-0.35|<2.145 we DO NOT reject H0. We believe the mean yields are the same for catalysts 1 and 2.

## Slide 104: Simple Experiments: Hypothesis Testing
Hypothesis Testing in Minitab
Stat
  Basic Statistics
Do catalyst example in Minitab
  Enter data in 2 columns
  First do F test to determine if variances are equal
  Then do t test to compare means

## Slide 105: Simple Experiments: Hypothesis Testing
1. Enter Data 2.Do F test
>Stat
>Basic Statistics
>2 Variances

## Slide 106: Simple Experiments: Hypothesis Testing
Test and CI for Two Variances: Catalyst 1, Catalyst 2
Method
Null hypothesis σ(Catalyst 1) / σ(Catalyst 2) = 1
Alternative hypothesis σ(Catalyst 1) / σ(Catalyst 2) ≠ 1
Significance level α = 0.05
Statistics
95% CI for
Variable N StDev Variance StDevs
Catalyst 1 8 2.386 5.691 (1.635, 4.611)
Catalyst 2 8 3.061 9.371 (1.634, 7.595)
Ratio of standard deviations = 0.779
Ratio of variances = 0.607
95% Confidence Intervals
CI for
CI for StDev Variance
Method Ratio Ratio
Bonett (0.380, 2.336) (0.145, 5.457)
Levene (0.305, 2.300) (0.093, 5.291)
Tests
Test
Method DF1 DF2 Statistic P-Value
Bonett 1 — 0.39 0.534
Levene 1 14 0.36 0.557

## Slide 107: Simple Experiments: Hypothesis Testing
Since p-value=0.565 > α=0.05, we DO NOT reject H0. We believe variances are equal
The P-value is the risk of wrongly rejecting the null hypothesis (it measures rareness of the event).
In general, reject H0 when p-value < α
Ratio of Variances (F-Statistic) = 0.638
*Can compare to Rejection Criteria for F-test*
OR
P-Value = 0.565

## Slide 108: P-value
We reject H0 when p-value < α
P-value is the smallest level of significance (i.e. α) that would lead to rejection of the null hypothesis H0 with the given sample.
P-value indicates how strongly we believe H0 or H1
  When p-value very small (i.e. near 0) we STRONGLY reject H0.
    We REALLY do not believe H0; We REALLY do believe H1
Thus, a P-value conveys much information about the weight of evidence against H0, and so a decision maker can draw a conclusion at any specified level of significance, α.

## Slide 109: Simple Experiments: Hypothesis Testing
3. Do t test
>Stat
>Basic Statistics
>2 Sample t
*Go into Options if need to check “Assume Equal Variances”
Note: Default is two-sided test. Can change to one-sided test.

## Slide 110: Simple Experiments: Hypothesis Testing
Two-Sample T-Test and CI: Catalyst 1, Catalyst 2
Two-sample T for Catalyst 1 vs Catalyst 2
N Mean StDev SE Mean
Catalyst 1 8 92.26 2.39 0.84
Catalyst 2 8 92.73 2.99 1.1
Difference = μ (Catalyst 1) - μ (Catalyst 2)
Estimate for difference: -0.48
95% CI for difference: (-3.37, 2.42)
T-Test of difference = 0 (vs ≠): T-Value = -0.35 P-Value = 0.730 DF = 14
Both use Pooled StDev = 2.7018
if p-value < α, reject H0
Since p-value=0.730 > α=0.05, we DO NOT reject H0. We believe means are equal

## Slide 111: Simple Experiments: Hypothesis Testing
Paired t test
Detects difference between matched pairs of data.
Each pair represents a block.
Remember: the objective of blocking is to reduce error by eliminating known sources of variation due to lot-to-lot, day-to-day, operator-to-operator, machine-to-machine, etc.

## Slide 112: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
We want to determine if shoe sole material A wears faster, slower, or the same as material B (measured as mm of wear after 60 days)
Data collection: Some shoes made with material A, some with material B. Ten (10) boys will wear the shoes for 60 days, after which time the wear (in mm) will be measured and analyzed.
How exactly to conduct experiment?
  5 boys wear shoes made of Material A, 5 boys wear shoes made of Material B?
  No! why?

## Slide 113: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
Remember, we want to evaluate the difference between the shoe sole materials, not the difference between boys.
We want to block out the difference between boys and concentrate the difference between materials.
  Block on boys
Can do this by giving each boy, 1 material A shoe and 1 material B shoe (randomize which is on left/right foot)
  use paired t test to analyze.

## Slide 114: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
Data

## Slide 115: Simple Experiments: Hypothesis Testing
Paired t test
Detects difference between matched pairs of data.
For each matched pair of data, find difference between responses
  For boys shoe example: dj = mat’l Bj – mat’l Aj for each boy j
Do hypothesis test to determine if μd=0 (i.e. no difference between means)
  H0: μd=0
  H1: μd≠0

## Slide 116: Simple Experiments: Hypothesis Testing
Paired t test
Test statistic:
  where
Rejection Criteria:
Reject H0 when |t0| > tα/2,n-1
Note: Here n is the number of differences, not the number of observations

## Slide 117: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
Why d=B-A?
Why not d=A-B?

## Slide 118: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
For α=0.05, t0.025,9 = 2.262
Since |3.36| > 2.262 we reject H0: μd =0.
Therefore we believe material A and material B do not wear the same

## Slide 119: Simple Experiments: Hypothesis Testing
Paired t test in Minitab
>Stat
>Basic Statistics
>Paired t

## Slide 120: Simple Experiments: Hypothesis Testing
Paired t test in Minitab
Paired T-Test and CI: Material A, Material B
Paired T for Material A - Material B
N Mean StDev SE Mean
Material A 10 10.630 2.451 0.775
Material B 10 11.040 2.518 0.796
Difference 10 -0.410 0.387 0.122
95% CI for mean difference: (-0.687, -0.133)
T-Test of mean difference = 0 (vs ≠ 0): T-Value = -3.35 P-Value = 0.009
Since p-value = 0.009 < α=0.05, we reject H0, therefore we believe there IS a difference in wear between materials A and B.

## Slide 121: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
What if we had evaluated the data using a t test to compare the mean wear of material A and material B (assume equal variances)?
Two-sample T for Material A vs Material B
N Mean StDev SE Mean
Material A 10 10.63 2.45 0.78
Material B 10 11.04 2.52 0.80
Difference = μ (Material A) - μ (Material B)
Estimate for difference: -0.41
95% CI for difference: (-2.74, 1.92)
T-Test of difference = 0 (vs ≠): T-Value = -0.37 P-Value = 0.716 DF = 18
Both use Pooled StDev = 2.4851

## Slide 122: Simple Experiments: Hypothesis Testing
Paired t test: Boys Shoe Example
Using a t test to compare the mean wear of material A and material B (assume equal variances) we conclude……
Since p-value=0.716 > α=0.05 we accept H0: μA=μB
Therefore, we believe no difference in wear between material A and B
However, this is not the correct analysis because it does not block out the differences between boys
  This example shows how you can reach the wrong conclusion if you do not use the proper test.

## Slide 123: Relationship between Hypothesis Test and CI
Close relationship between CI and hypothesis test
For a specific significance level, α, a CI is more informative than performing a hypothesis test.
  The decision made by the hypothesis test can be deduced from the confidence interval by looking to see whether μ0 is inside the confidence interval or not.
Thus the confidence interval portrays the decisions made by hypothesis test for all possible values of μ0 (for a given α)
However, for a specific sample, a hypothesis test is more informative than performing a CI because the hypothesis test can quickly show decisions (accept or reject) for a variety of significance levels, α.

## Slide 124: HW#1 here
Due date =
Unless otherwise stated, you may use Minitab to do HW assignments
If submitting HW electronically, submit one (1) file only !!!
Can copy Minitab output and paste into MS Word. Use ‘Courier New’ font when pasting Minitab output in MS Word.
Indicate where the answer is located in Minitab output (circle, highlight, etc.)
Submit Word, Excel, or PDF files (Minitab supplemental files are ok). NO .jnt files!

## Slide 125: Simple Experiments and Design of Experiments
We reviewed several simple two-sample, comparative experiments
  Compare response at two factor levels
    Compare mean yield rates for two catalysts
    Compare mean wear for two shoe sole materials
This DOE course extends these simple experiments to more than two factor levels
  The main analysis technique we’ll use in this class, ANOVA, is an extension of a t test

## Slide 126: What If There Are More Than Two Factor Levels?
The t-test does not directly apply
There are lots of practical situations where there are either more than two levels of interest, or there are several factors of simultaneous interest
The analysis of variance (ANOVA) is the appropriate analysis “engine” for these types of experiments – Chapter 3, textbook
The ANOVA was developed by Fisher in the early 1920s, and initially applied to agricultural experiments
Used extensively today for industrial experiments

## Slide 127: Single Factor Designed Experiment
Does factor affect the response?
Collect observations (i.e. measure response) at each of a levels (or treatments or settings) of the factor through replication (repeated experimentation).
    n1 observations at level 1 n1 replicates at level 1
    n2 observations at level 2 n2 replicates at level 2
    •••
    na observations at level a na replicates at level a
Total observations = N = n1 + n2 + ••• + na
If n1 = n2 = ••• = na then balanced design, otherwise unbalanced design
When all N observations collected in random order, then completely randomized design (CRD)

## Slide 128: Single Factor Designed Experiment
Level (treatment) | Observations Yij = ijth observation (factor level i, replicate j) |  |  |  | Totals | Averages
1 | Y11 | Y12 | • • • | Y1n1 | Y 1• | Y 1•
2 | Y21 | Y22 | • • • | Y2n2 | Y 2• | Y 2•
 | • • • | • • • | • • • | • • • | • • • | • • •
a | Ya1 | Ya2 | • • • | Yana | Y a• | Y a•
 |  |  |  |  | Y•• | Y••
Use ANOVA (Analysis of Variance) to determine if factor affects response
Objective of ANOVA is to test hypotheses about the equality of the a factor level means
Dot (•) indicates we sum over that subscript

## Slide 129: Chapter 3 The Analysis of Variance (ANOVA)

## Slide 130: The Analysis of Variance (ANOVA)
Objective of ANOVA is to test hypotheses about the equality of the a factor level means
μ1
μ2
μ3
μ2
μ2
μ3
μ3
μ1
μ1
H0: factor does not affect response
H1: factor does affect response
H0: μ1 = μ2 = ••• = μa
H1: at least one mean is different
Distribution of responses from at 3 factor levels

## Slide 131: The Analysis of Variance (ANOVA)
The basic single-factor ANOVA model is
Yij = ijth observation (factor level i, replicate j). A random variable.
μ = the overall mean common to all factor levels. A constant.
τi = the ith factor level effect. A constant for each factor level, i.
εij = random error. A random variable. εij~ NID(0, σ2)
Therefore, Yij ~ NID (μ+τi, σ2)

## Slide 132: The ANOVA Normality Assumption
The ANOVA is a parametric test – it assumes the data (i.e. responses) are Normally distributed
  ANOVA assumes data for each factor level is normally distributed; not overall data
  If response is not normally distributed, an ANOVA may increase the chance of a false positive result
HOWEVER, the ANOVA is not very sensitive to moderate deviations from normality
  simulation studies, using a variety of non-normal distributions, have shown that the false positive rate is not affected very much by this violation of the normality assumption
Can do a histogram of responses for each factor level
  if they look Normally distributed, proceed with ANOVA. If not, try a data transformation. If still not Normal, use non-parametric analysis.
  Many data sets would fail a goodness of fit test for Normality and still be appropriate for ANOVA

## Slide 133: The Analysis of Variance (ANOVA)
The name “analysis of variance” stems from a partitioning of the total variability in the response variable into components
Total variability is measured by the total sum of squares:

## Slide 134: The Analysis of Variance (ANOVA)
The basic ANOVA partitioning is:
SSTotal
SSFactor
SSError
SSTotal = SSFactor + SSError

## Slide 135: Total Variability: SSTotal
Factor Level 1 Factor Level 2 Factor Level 3

## Slide 136: Between Factor Level Variability: SSFactor
Factor Level 1 Factor Level 2 Factor Level 3

## Slide 137: Within Factor Level Variability (i.e. random error): SSError
Factor Level 1 Factor Level 2 Factor Level 3

## Slide 138: The Analysis of Variance (ANOVA)
A large value of SSFactor reflects large differences in factor level means (i.e. factor DOES affect response)
A small value of SSFactor likely indicates no differences in factor level means (i.e. factor DOES NOT affect response)
To reduce rounding errors, use following formulas:
SSTotal = SSFactor + SSError

## Slide 139: The Analysis of Variance (ANOVA)
Objective of ANOVA is to test hypotheses about the equality of the a factor level means
Formal statistical hypotheses are:
      H0: μ1 = μ2 = • • • = μa
      H1: At least one mean is different
While sums of squares cannot be directly compared to test the hypothesis of equal means, mean squares can be compared.

## Slide 140: The Analysis of Variance (ANOVA)
A mean square is a sum of squares divided by its degrees of freedom:

## Slide 141: The Analysis of Variance (ANOVA)
Use F test to compare variances
The reference distribution for F0 is the Fα,a-1,N-a distribution
Reject the null hypothesis (H0: equal factor level means) if

## Slide 142: ANOVA Table
Source of Variation | SS | df | MS | F
Factor | SSFactor | a-1 | MSFactor | 
Error | SSError | N-a | MSError | 
Total | SSTotal | N-1 |  | 

## Slide 143: ANOVA
Basic Idea….
Compare average response for each factor level
If big difference between factor level average responses, we believe the factor does affect the response (i.e. it matters which level you choose because different levels can lead to very different responses)
How big a difference between factor level average responses needed for us to believe factor affects response?
  Compare variability between factor level average responses to random error (i.e. variability within factor levels)
  Use statistical test to do above comparison

## Slide 144: ANOVA Example
Blood Coagulation Example
Does diet affect the blood coagulation times of mice?
Test 4 diets (A, B, C, D) on 24 mice. Each mouse receives one diet. Data collected in completely randomized order.
  Response: Blood coagulation time
  Factor: diet
  Factor levels: diet A, diet B, diet C, diet D
  Replicates: diet A = 4, diet B = 6, diet C = 6, diet D = 8
The resulting blood coagulation times (in minutes) follow
Unbalanced design
Diet | Blood Coagulation Time (min) |  |  |  |  |  |  |  | Total | Average
A | 62 | 60 | 59 | 63 |  |  |  |  | 244 | 61
B | 63 | 67 | 71 | 64 | 65 | 66 |  |  | 396 | 66
C | 68 | 66 | 71 | 67 | 68 | 68 |  |  | 408 | 68
D | 56 | 62 | 60 | 61 | 63 | 64 | 63 | 59 | 488 | 61
 |  |  |  |  |  |  |  |  | 1536 | 64

## Slide 145: ANOVA Example
Blood Coagulation Example
Summarized Results Table
Results in Order Collected
i.e. randomized data collection
Diet | Blood Coagulation Time (min) |  |  |  |  |  |  | 
A | 62 | 60 | 59 | 63 |  |  |  | 
B | 63 | 67 | 71 | 64 | 65 | 66 |  | 
C | 68 | 66 | 71 | 67 | 68 | 68 |  | 
D | 56 | 62 | 60 | 61 | 63 | 64 | 63 | 59

## Slide 146: ANOVA Example
H0: μA=μB=μC=μD
H1: at least one mean is different
a = 4 N = 24
H0: factor does not affect response
H1: factor does affect response

## Slide 147: ANOVA Example
ANOVA Table
H0: μA=μB=μC=μD
Reject H0 if F0 > Fα,a-1,N-a
F0.05,3,20 = 3.10
Since 13.57 > 3.10 we reject H0
We believe diet does affect blood coagulation time
Source of Variation | SS | df | MS | F
Diet | 228 | 3 | 76 | 13.57
Error | 112 | 20 | 5.6 | 
Total | 340 | 23 |  | 
H0: factor does not affect response
H1: factor does affect response

## Slide 148: Cake Baking Example
Does # eggs affect cake height?
Response: cake height (inches)
Factor: # eggs
Factor levels: 2, 3, 4 eggs
Replicates: 5
Data collected in completely randomized order
H0: μ2eggs = μ3eggs = μ4eggs
H1: at least one mean is different
Balanced design
Your best guess: Does the number of eggs affect cake height?
Yes No Why?

## Slide 149: Cake Baking Example
ANOVA Table
Does the number of eggs affect cake height?
Use α = 0.05 F0.05,2,12 = 3.89
H0: μ2eggs = μ3eggs = μ4eggs
Since 21.91 > 3.89 we reject H0
  i.e. we reject the hypothesis that the average cake height is approximately the same whether we use 2, 3, or 4 eggs
Conclude number of eggs does affect cake height
H0: factor does not affect response
H1: factor does affect response
Source of Variation | SS | df | MS | F
# eggs | 1.577 | 2 | 0.789 | 21.91
Error | 0.432 | 12 | 0.036 | 
Total | 2.009 | 14 |  | 

## Slide 150: Cake Baking Example
Does # eggs affect cake height?
Response: cake height (inches)
Factor: # eggs
Factor levels: 2, 3, 4 eggs
Replicates: 5
Data collected in completely randomized order
H0: μ2eggs = μ3eggs = μ4eggs
H1: at least one mean is different
Balanced design
Your best guess: Does the number of eggs affect cake height?
Yes No Why?

## Slide 151: Cake Baking Example
ANOVA Table
Does the number of eggs affect cake height?
Use α = 0.05 F0.05,2,12 = 3.89
H0: μ2eggs = μ3eggs = μ4eggs
Since 0.46 < 3.89 we accept H0
  i.e. we accept the hypothesis that the average cake height is approximately the same whether we use 2, 3, or 4 eggs
Conclude number of eggs does not affect cake height
H0: factor does not affect response
H1: factor does affect response
Source of Variation | SS | df | MS | F
# eggs | 1.577 | 2 | 0.789 | 0.46
Error | 20.392 | 12 | 1.699 | 
Total | 21.969 | 14 |  | 

## Slide 152: Post-ANOVA Comparison of Means
The analysis of variance tests the hypothesis of equal factor level means
If that hypothesis is rejected, we don’t know which specific means are different
Determining which specific means differ following an ANOVA is called the multiple comparisons problem
There are lots of ways to do this…see text, Section 3-5
We will use pairwise comparison of means
  Confidence intervals
  Tukey test

## Slide 153: Comparison Among Factor Level Means
Confidence Interval comparison of Means
100(1-α)% CI on difference between any 2 factor level means, μi-μj
If 0 in interval, then NO significant difference between factor level means
d.f. for MSE

## Slide 154: Comparison Among Factor Level Means
For blood coagulation example
Find 90% CI on difference in blood coagulation times between diets A and B
(-7.635, -2.365)
Significant difference in the average blood coagulations times produced by diets A and B?

## Slide 155: Comparison Among Factor Level Means
Tukey test
Compare all pairs of factor level means
Two factor level means are significantly different if
Where a= # factor levels; f = d.f. for MSE
Based on studentized range statistic – a table lookup value

## Slide 156: Comparison Among Factor Level Means
Tukey test for blood coagulation example
q0.05(4,20)=3.96 from Table VII
A vs B
A vs C
Pairs sig. different?

## Slide 157: Comparison Among Factor Level Means
A vs D
B vs C
B vs D
C vs D
Pairs sig. different?

## Slide 158: Comparison Among Factor Level Means
Results can be expressed graphically
60 62 64 66 68 70
Bars under factor level labels indicate pairs are NOT significantly different
To maximize blood coagulation time, choose diet B or C? diet A or B?

## Slide 159: Pairwise Comparisons
Possible to get seemingly paradoxical results
1 and 2 not significantly different
1 and 3 not significantly different
Does this imply 2 and 3 not significantly different? NO!
2 and 3 are significantly different
Saying a pair is not significantly different is not the same as saying they are equal.
  The transitive property (A=B and B=C therefore A=C) is not in effect
We know 2 and 3 are significantly different and 1 is somewhere between 2 and 3
Choose either 2 or1 to maximize response
Which levels maximize avg. response?
Which levels minimize avg. response?

## Slide 160: Pairwise Comparisons
It is possible for ANOVA and Pairwise Comparisons to contradict
  ANOVA indicates factor significance (p-value < α) but Tukey test indicates no significantly different factor levels at α
  ANOVA indicates no factor significance (p-value > α) but Tukey test indicates significantly different factor levels at α
Tukey test uses family error rate
  the chances of making a type I error for a series of comparisons is greater than the error rate for any one comparison alone.
    Family error = 1 – (1- individual error) a where a = # factor levels
    For a=5 levels and individual error =0.05, family error = 1 – (1 - 0.05)5 = 0.2262
    For a=5 levels and family error =0.05, individual error = 1 - 5√(1 – 0.05) = 0.0102
  To counter this higher family error rate, Tukey's method adjusts the confidence level for each individual interval so that the resulting simultaneous confidence level is equal to the value you specify.

## Slide 161: ANOVA in Minitab
Enter data in worksheet
  One column for factor levels
    Older versions of Minitab require factor levels to be numeric
  One column for observations
  Enter data in actual run order

## Slide 162: ANOVA in Minitab
Stat
  ANOVA
    General Linear Model
      Fit General Linear Model

## Slide 163: ANOVA in Minitab
General Linear Model: time versus diet
Factor Type Levels Values
diet fixed 4 A, B, C, D
Analysis of Variance for time, using Adjusted SS for Tests
Source DF Seq SS Adj SS Adj MS F P
diet 3 228.000 228.000 76.000 13.57 0.000
Error 20 112.000 112.000 5.600
Total 23 340.000
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.36643 67.06% 62.12% 53.46%
Fits and Diagnostics for Unusual Observations
Obs time Fit Resid Std Resid
5 71.00 66.00 5.00 2.31 R
9 56.00 61.00 -5.00 -2.26 R
R denotes an observation with a large standardized residual.
When p-value < α we reject H0 (i.e. conclude factor DOES affect response)

## Slide 164: p-value
p-value = probability of obtaining this F0 or larger when the null hypothesis is true
We reject H0 (i.e. factor is significant) for all p-value < α
  Reject H0 (i.e. factor is significant) for small p-values
  p = 0.03 accept or reject H0? Depends on α
    When α = 0.05, reject H0
    When α = 0.01, accept H0
Relationship between F0 and p-value
  As F0 increases, p-value decreases
  As F0 decreases, p-value increases
  As F0 approaches Fα,v1,v2, p-value approaches α
Same α

## Slide 165: Minitab: Tukey procedure
Stat
  ANOVA
    GLM: General Linear Model
      Comparisons
To change confidence level

## Slide 166: Minitab: Tukey Test
Tukey Simultaneous Tests
Response Variable time
All Pairwise Comparisons among Levels of diet
Tukey Simultaneous Tests for Differences of Means
Difference
of diet Difference SE of Simultaneous Adjusted
Levels of Means Difference 95% CI T-Value P-Value
B - A 5.00 1.53 ( 0.72, 9.28) 3.27 0.018
C - A 7.00 1.53 ( 2.72, 11.28) 4.58 0.001
D - A -0.00 1.45 ( -4.06, 4.06) -0.00 1.000
C - B 2.00 1.37 ( -1.83, 5.83) 1.46 0.477
D - B -5.00 1.28 ( -8.58, -1.42) -3.91 0.004
D - C -7.00 1.28 (-10.58, -3.42) -5.48 0.000
Individual confidence level = 98.89%
P-value < α? then sig. diff.

## Slide 167: Multiple Comparisons
Tukey Test
  Often helpful to analyze Minitab Tukey Test output in organized fashion
  Start with level with maximum (minimum) avg. response; compare to levels in decreasing (increasing) order; stop when first significant difference found
  e.g. Which diet(s) maximize blood coagulation time?

## Slide 168: Minitab: Tukey Test
Tukey Simultaneous Tests
Response Variable time
All Pairwise Comparisons among Levels of diet
Tukey Simultaneous Tests for Differences of Means
Difference
of diet Difference SE of Simultaneous Adjusted
Levels of Means Difference 95% CI T-Value P-Value
B - A 5.00 1.53 ( 0.72, 9.28) 3.27 0.018
C - A 7.00 1.53 ( 2.72, 11.28) 4.58 0.001
D - A -0.00 1.45 ( -4.06, 4.06) -0.00 1.000
C - B 2.00 1.37 ( -1.83, 5.83) 1.46 0.477
D - B -5.00 1.28 ( -8.58, -1.42) -3.91 0.004
D - C -7.00 1.28 (-10.58, -3.42) -5.48 0.000
Individual confidence level = 98.89%
P-value < α? then sig. diff.

## Slide 169: Minitab: Tukey Test
Tukey Simultaneous Tests
Response Variable time
All Pairwise Comparisons among Levels of diet
Tukey Simultaneous Tests for Differences of Means
Difference
of diet Difference SE of Simultaneous Adjusted
Levels of Means Difference 95% CI T-Value P-Value
B - A 5.00 1.53 ( 0.72, 9.28) 3.27 0.018
C - A 7.00 1.53 ( 2.72, 11.28) 4.58 0.001
D - A -0.00 1.45 ( -4.06, 4.06) -0.00 1.000
C - B 2.00 1.37 ( -1.83, 5.83) 1.46 0.477
D - B -5.00 1.28 ( -8.58, -1.42) -3.91 0.004
D - C -7.00 1.28 (-10.58, -3.42) -5.48 0.000
Individual confidence level = 98.89%
Interval contains 0? then no sig. diff.

## Slide 170: Minitab: Tukey Test

## Slide 171: Minitab: Tukey Grouping
Grouping Information Using the Tukey Method and 95% Confidence
diet N Mean Grouping
C 6 68 A
B 6 66 A
A 4 61 B
D 8 61 B
Means that do not share a letter are significantly different.
Choose diet C or B to maximize blood coagulation time
Choose diet A or D to minimize blood coagulation time

## Slide 172: Minitab Demo Here
Demo ANOVA in Minitab
  Worksheet ‘blood.mtw’
Demo Tukey Test & CI in Minitab

## Slide 173: Another example
Problem 3-19
Four chemists are asked to determine the percentage of methyl alcohol in a certain chemical compound. Each chemist makes three determinations. The following data is collected in a completely randomized order
Do the chemists differ significantly?
  Response?
  Factor?
  Factor levels?
  # replicates?

## Slide 174: Problem 3-19 (cont.)
From Minitab
General Linear Model: % MA versus chemist
Factor Type Levels Values
chemist fixed 4 1, 2, 3, 4
Analysis of Variance for % MA
Source DF Seq SS Adj SS Adj MS F P
chemist 3 1.0446 1.0446 0.3482 3.25 0.081
Error 8 0.8582 0.8582 0.1073
Total 11 1.9028
Conclusion? Do the chemists differ?
H0: μ1=μ2=μ3=μ4
Do pairwise comparison (Tukey) of the chemists?

## Slide 175: HW#2 here
Due date =
Unless otherwise stated, you may use Minitab to do HW assignments
If submitting HW electronically, submit one (1) file only !!!
Can copy Minitab output and paste into MS Word. Use ‘Courier New’ font when pasting Minitab output in MS Word.
Indicate where the answer is located in Minitab output (circle, highlight, etc.)
Data sets can be copied from assignment document and pasted into Excel or Minitab. Some data sets may need to be rearranged before conducting an analysis in Minitab

## Slide 176: ANOVA Model Adequacy Checking
ANOVA based on several assumptions
Check to see if these assumptions are valid. If not, do not use ANOVA.
Random error, εij, assumed to be NID(0, σ2)
  Error normally distributed
  Error independently distributed
  Error has mean of 0
  Error has constant variance

## Slide 177: Model Adequacy Checking
We use residuals, eij, as estimator of random error εij
Residual is difference between actual observation and estimated observation
Calculation of estimated observation depends on model
  For single factor ANOVA:
So, for single factor ANOVA

## Slide 178: Model Adequacy Checking
each observation has a residual (i.e. there are N residuals)
Residual is and for single factor ANOVA
Residuals for Blood Coagulation example (shown in sorted order, not random order)

## Slide 179: Model Adequacy Checking
Random error, εij, assumed to be NID(0, σ2)
Residuals Normally distributed?
  Check normal probability plot of residuals
    Straight line?
Residuals have a mean of zero?
  Check normal probability plot of residuals
    Centered around zero?
Residuals independently distributed?
  Check residuals vs run order plot
    No patterns?
Residuals have a constant variance?
  Check residuals vs predicted value (fit) plot
    No patterns?

## Slide 180: Model Adequacy Checking
General Linear Model Window
  Graphs

## Slide 181: Model Adequacy Checking

## Slide 182: Residual Analysis Residuals normally distributed with mean of 0?
Normal probability plot – straight line centered at 0?
  Moderate departures from normality OK for fixed effects model
  If really not a straight line (i.e. not normally distributed) try transformation; if normality assumption still not good, use nonparametric test
  Outliers
    Common occurrence
    Make sure data collected and recorded properly
    Do not automatically discard outliers
    Possible outliers: observations with standardized residuals greater than 3 or less than -3 (we expect 99.73% of observations to have standardized residuals between -3 and 3)
Standardized residual ij =

## Slide 183: Residual Analysis Nonnormal responses and transformations
If response not Normally distributed, then can try transformation
  ANOVA is OK for moderate departures from normality
  Nonnormal Responses relatively common in practice
    Count # defects
    Distance from target skewed resp. distr. (bounded on 1 side)
    Any %
  Transform the response, Y, values
    Which transformation to use? Trial and error or Box-Cox method
    Common transformations: 1/Y, √Y, 1/√Y, ln(Y), log10(Y)
  Conclusions apply to transformed data
  Do reverse transformation

## Slide 184: Residual Analysis Nonnormal responses and transformations
Box-Cox Transformation Method
  Transform response, Y, using power family of transformations:
  What λ to use?
    Choose λ to transform response to normality
    Minitab will determine best λ value
  Cannot use Box-Cox transformation if any responses are 0 or negative
    Add constant to responses to make > 0
    Be sure to subtract constant (and do reverse transformation) when drawing conclusions and making predictions

## Slide 185: Residual Analysis Nonnormal responses and transformations
Transform response, Y, using Box-Cox transformation in Minitab

## Slide 186: Residual Analysis Nonnormal responses and transformations
Box-Cox transformation in Minitab
  Transform response in >Regression >General Regression
  Then use transformed response in ANOVA
In Minitab:
Stat
  Regression
    Regression
      Fit Regression Model
        Options

## Slide 187: Residual Analysis Nonnormal responses and transformations
In Minitab:
Stat
  Regression
    Regression
      Fit Regression Model
        Options
Box-Cox transformation in Minitab
  Transform response in >Regression >General Regression
  Then use transformed response in ANOVA
Store Transformed Response

## Slide 188: Residual Analysis Nonnormal responses and transformations
General Regression Analysis: y versus factor
Box-Cox transformation
Rounded λ 0
Estimated λ 0.0415197
95% CI for λ (-0.297980, 0.369020)
Regression Equation
ln(y) = 2.335 + 0.0005 factor
Box-Cox transformation in Minitab
  Use value of λ that makes practical sense – use rounded λ
ln(y) = BOXC1
e.g. ln(7.015) = 1.94799

## Slide 189: Residual Analysis Nonnormal responses and transformations
Box-Cox transformation in Minitab
  Transform response in >Regression >General Regression
  Then use transformed response in ANOVA
  Remember: ANOVA conclusions apply to transformed data
  Do reverse transformation

## Slide 190: Residual Analysis Residuals independently distributed?
Residual vs time – random scatter plot?
  If not a random scatter plot indicates correlation between residuals – i.e. not independently distributed
  Causes of correlation
    Skill of subjects or experimenter changes over time
    Equipment wear will change responses over time
    Experiment not properly randomized
Time
eij
0
Time
eij
0
Positive correlation
Negative correlation

## Slide 191: Residual Analysis Residuals have constant variance?
Statistical test - Bartlett’s Test
Residual vs fitted value – random scatter plot?
  Sometimes variance of observation changes as magnitude of observation increases (i.e. residuals correlated with magnitude of response)
If residual variance nonconstant, then can try transformation
  Transform the response, Y, values
    Which transformation to use? Box-Cox method
    Conclusions apply to transformed data
    Do reverse transformation
Fitted Y
eij
0
Fitted Y
eij
0
Funnel – nonconstant variance

## Slide 192: Residual Analysis nonconstant residual variance and transformations
variance stabilizing transformation example

## Slide 193: Residual Analysis nonconstant residual variance and transformations
variance stabilizing transformation example
Box-Cox transformation of the response with estimated lambda = 0.200235
The 95% CI for lambda is (-0.201265, 0.604735)
Rounded lambda = 0 used in the regression analysis
Regression Equation
ln(y) = 2.43901 - 0.504436 factor level
ln(Y) = BOXC2
e.g. ln(6.09) = 1.80665

## Slide 194: Residual Analysis
In Minitab
Stat
  ANOVA
    General Linear Model (Fit General Linea Model)
      Graphs
        Four in one

## Slide 195: Minitab residual analysis for blood coagulation example

## Slide 196: Minitab residual analysis for problem 3-19 (Chemists)

## Slide 197: Regression Analysis
Now we are ready to draw practical conclusions
Use Regression Analysis to build a mathematical model relating response to factor(s)
  Simple linear regression (single factor)
  Multiple linear regression

## Slide 198: Regression Analysis
An experimenter is often interested in how a particular variable depends upon one or more of the other variables.
Modeling is often performed by finding a functional relationship between the expected value of a dependent variable, Y, and a set of independent variables, Xi.
How does X affect Y? What is the effect of X on Y?
Linear Regression is a modeling technique in which the expected value of a dependent variable is modeled as a linear combination of a set of independent variables.
Many problems in engineering and science involve exploring the relationships between two or more variables.

## Slide 199: Regression Analysis
Example
A company that makes paper grocery bags is interested in improving the tensile strength of their bags. Specifically they are interested in the relationship between the hardwood concentration in the pulp and the tensile strength of the bag.
Regression analysis can be used to build a model to relate tensile strength (Y) to hardwood concentration (X).

## Slide 200: Regression Analysis
Consider ANOVA
General Linear Model: strength versus hardwood
Factor Type Levels Values
hardwood fixed 4 5, 10, 15, 20
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
hardwood concentration 3 382.8 127.597 19.61 0.000
Error 20 130.2 6.508
Total 23 513.0

## Slide 201: Regression Analysis
ANOVA tells us hardwood concentration affects bag tensile strength
What is their relationship? Develop mathematical model relating hardwood concentration and tensile strength

## Slide 202: Regression Analysis
Based on the scatter diagram, it is probably reasonable to assume that the variable Y is related to X by the following simple linear regression model :
Y = β0 + β1X + ε
where the slope, β1, and intercept, β0, of the line are called regression coefficients and where  is the random error term.
 ~NID (0, σ2)

## Slide 203: Simple Linear Regression
The case of simple linear regression considers a single regressor or predictor or independent variable X and a dependent or response variable Y.
  1 term in regression model (not counting constant)
How to fit line to data? How to find values for slope, β1, and intercept, β0?
find slope, β1, and intercept, β0, of best fitting line.

## Slide 204: Simple Linear Regression
Used when demand is linearly increasing or decreasing over time
Find ‘best’ fitting line to data

## Slide 205: Simple Linear Regression
The method of least squares is used to estimate the parameters, 0 and 1 by minimizing the sum of the squares of the vertical deviations in Figure below.
Figure Deviations of the data from the estimated regression model.

## Slide 206: Simple Linear Regression
The sum of the squares of the deviations of the observations from the true regression line is
How to find 0 and 1 that minimize L?

## Slide 207: Simple Linear Regression
The least squares estimates of the intercept and slope in the simple linear regression model are
Fitted or estimated regression line is

## Slide 208: Simple Linear Regression
Fit a simple linear regression model to paper bag example

## Slide 209: Simple Linear Regression
Y = 7.25 + 0.697*X
Strength = 7.25 + 0.697*Hardwood

## Slide 210: Regression Analysis in Minitab
Data in 2 columns: response (Y) & factor (X)
Stat
  Regression
    Regression
      Fit Regression Model

## Slide 211: Regression Analysis in Minitab
Regression Analysis: strength versus hardwood
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 364.01 364.008 53.76 0.000
hardwood concentration 1 364.01 364.008 53.76 0.000
Error 22 148.95 6.770
Lack-of-Fit 2 18.78 9.392 1.44 0.260
Pure Error 20 130.17 6.508
Total 23 512.96
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.60201 70.96% 69.64% 65.18%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 7.25 1.30 5.57 0.000
hardwood concentration 0.6967 0.0950 7.33 0.000 1.00
Regression Equation
tensile strength = 7.25 + 0.6967 hardwood concentration

## Slide 212: Prediction of New Observations
If x0 is the value of the regressor variable of interest,
is the point estimator of the new or future value of the response, Y0.
Predict bag strength for a hardwood concentration of 8%
Strength = 7.25 + 0.697(8) = 12.826

## Slide 213: Prediction of New Observations
and where
A 100(1-α)% prediction interval on a future observation Y0 at the value x0 is given by
where

## Slide 214: Prediction of New Observations
Find a 95% PI for the tensile strength at a hardwood concentration of x0 = 8%
(7.28, 18.37)
n =24

## Slide 215: Regression Analysis in Minitab
Regression Analysis: strength versus hardwood
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 364.01 364.008 53.76 0.000
hardwood concentration 1 364.01 364.008 53.76 0.000
Error 22 148.95 6.770
Lack-of-Fit 2 18.78 9.392 1.44 0.260
Pure Error 20 130.17 6.508
Total 23 512.96
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.60201 70.96% 69.64% 65.18%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 7.25 1.30 5.57 0.000
hardwood concentration 0.6967 0.0950 7.33 0.000 1.00
Regression Equation
tensile strength = 7.25 + 0.6967 hardwood concentration

## Slide 216: Regression Analysis in Minitab
Prediction intervals in Minitab
  Stat
    Regression
      Regression
        Predict
Change settings (i.e. 95%, etc) here

## Slide 217: Regression Analysis in Minitab
Prediction for tensile strength
Regression Equation
tensile strength = 7.25 + 0.6967 hardwood concentration
Variable Setting
hardwood concentration 8
Fit SE Fit 95% CI 95% PI
12.8233 0.681839 (11.4093, 14.2374) (7.24490, 18.4018)
Difference between CI and PI:
Prediction Interval: Represents a range that a single new observation is likely to fall given specified settings of the predictors.
Confidence interval of the prediction: Represents a range that the mean response is likely to fall given specified settings of the predictors.
The PI is always wider than the corresponding CI because of the added uncertainty involved in predicting a single response versus the mean response.

## Slide 218: Regression Analysis
We can fit a regression line to any data.
Is line a good fit? Will it give good predictions?
Does X have a significant effect on Y?

## Slide 219: Adequacy of the Regression Model
Use statistical hypotheses tests about the model parameters to assess the adequacy of a linear regression model
We can perform hypothesis testing on both the slope, β1, and the intercept, β0
The most important hypothesis test is on the slope, β1 :
      H0: β1 = 0
      H1: β1 ≠ 0
This hypothesis relates to the significance of regression.
Failure to reject H0 is equivalent to concluding that there is no linear relationship between X (factor) and Y (response).

## Slide 220: Hypothesis Tests in Simple Linear Regression
The hypothesis H0: 1 = 0 is not rejected.
The hypothesis H0: 1 = 0 is rejected.

## Slide 221: Hypothesis Tests in Simple Linear Regression
To test this significance of regression hypothesis we do an ANOVA on the regression model
Partition total sum of squares into sum of squares for regression model and sum of squares error
SST = SSR + SSE
Test statistic = F0 = MSR/MSE
Do ANOVA on Regression equation using Minitab
  How much response variability explained by regression equation

## Slide 222: Regression Analysis in Minitab
Regression Analysis: strength versus hardwood
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 364.01 364.008 53.76 0.000
hardwood concentration 1 364.01 364.008 53.76 0.000
Error 22 148.95 6.770
Lack-of-Fit 2 18.78 9.392 1.44 0.260
Pure Error 20 130.17 6.508
Total 23 512.96
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.60201 70.96% 69.64% 65.18%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 7.25 1.30 5.57 0.000
hardwood concentration 0.6967 0.0950 7.33 0.000 1.00
Regression Equation
tensile strength = 7.25 + 0.6967 hardwood concentration
If P-value < α, then reject H0: β1=0
If P-value < α, then believe there is a sig. relationship between X & Y

## Slide 223: ANOVA NOTES
ANOVA from designed experiment NOT same as ANOVA from regression
In general, ANOVA shows how much variability in data can be explained and how much cannot (random error)
Designed experiment ANOVA
  How much variability explained by different factor levels
Regression ANOVA shows
  How much variability explained by regression equation
Designed experiment ANOVA and Regression ANOVA will have same SSTotal
However SSregression ≠ SSfactor AND dfregression ≠ dffactor

## Slide 224: 2 different ANOVAs
ANOVA from Designed Experiment
General Linear Model: strength versus hardwood
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
hardwood concentration 3 382.8 127.597 19.61 0.000
Error 20 130.2 6.508
Total 23 513.0
ANOVA from Regression Analysis
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 364.01 364.008 53.76 0.000
hardwood concentration 1 364.01 364.008 53.76 0.000
Error 22 148.95 6.770
Lack-of-Fit 2 18.78 9.392 1.44 0.260
Pure Error 20 130.17 6.508
Total 23 512.96

## Slide 225: Adequacy of the Regression Model
Coefficient of Determination (R2)
The quantity R2 is called the coefficient of determination and is often used to judge the adequacy of a regression model
0  R2  1 or 0%  R2  100%
We often refer to R2 as the amount of variability in the data (i.e. responses) explained or accounted for by the regression model.

## Slide 226: Adequacy of the Regression Model
Higher R2 values indicate a better fit of line to data
We often refer to R2 as the amount of variability in the data explained or accounted for by the regression model
No universal cut-off or threshold R2 value to define ‘good fitting’ model versus ‘bad fitting model
Y
X
Y
X
Higher R2
Lower R2

## Slide 227: Adequacy of the Regression Model
Coefficient of Determination (R2)
For the bag strength regression model,
R2 = SSR/SST
= 364.01 / 512.96
= 0.710
Thus, the model accounts for 71.0% of the variability in the responses (tensile strengths).

## Slide 228: Regression Analysis in Minitab
S represents the standard deviation of the distance that data values fall from the regression line (i.e. standard deviation of the residuals). The better the equation predicts the response, the lower S is.
S = √MSE and is used to calculate PI
Regression Analysis: strength versus hardwood
The regression equation is
strength = 7.25 + 0.697 hardwood
Predictor Coef SE Coef T P
Constant 7.250 1.301 5.57 0.000
hardwood 0.69667 0.09501 7.33 0.000
S = 2.60201 R-Sq = 71.0% R-Sq(adj) = 69.6%
Analysis of Variance
Source DF SS MS F P
Regression 1 364.01 364.01 53.76 0.000
Residual Error 22 148.95 6.77
Total 23 512.96

## Slide 229: Regression Analysis in Minitab
Regression Analysis: strength versus hardwood
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 364.01 364.008 53.76 0.000
hardwood concentration 1 364.01 364.008 53.76 0.000
Error 22 148.95 6.770
Lack-of-Fit 2 18.78 9.392 1.44 0.260
Pure Error 20 130.17 6.508
Total 23 512.96
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.60201 70.96% 69.64% 65.18%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 7.25 1.30 5.57 0.000
hardwood concentration 0.6967 0.0950 7.33 0.000 1.00
Regression Equation
tensile strength = 7.25 + 0.6967 hardwood concentration
S represents the standard deviation of the distance that data values fall from the regression line (i.e. standard deviation of the residuals). The better the equation predicts the response, the lower S is.
S = √MSE and is used to calculate PI

## Slide 230: R2 vs P-value
R2 measures amount of variability in the data explained by the regression model.
  Closeness of data to regression model
P-value indicates whether relationship exists between X and Y
  non-zero slope

## Slide 231: Adequacy of the Regression Model
Regression analysis based on several assumptions
Check to see if these assumptions are valid.
Random error, εij, assumed to be NID(0, σ2)
  Error normally distributed
  Error independently distributed
  Error has mean of 0
  Error has constant variance

## Slide 232: Adequacy of the Regression Model
We use residuals, eij, as estimator of random error εij
Residual is difference between actual observation and estimated observation
Calculation of estimated observation depends on model
  For simple linear regression:
So, for simple linear regression

## Slide 233: Adequacy of the Regression Model
Residuals Normally distributed?
  Check normal probability plot of residuals
    Straight line? If not, use Box-Cox transformation
Residuals have a mean of zero?
  Check normal probability plot of residuals
    Centered around zero?
Residuals independently distributed?
  Check residuals vs run order plot
    No patterns?
Residuals have a constant variance?
  Check residuals vs predicted value (fit) plot
    No patterns? If not, use Box-Cox transformation

## Slide 234: Adequacy of the Regression Model
Bag Strength Example
Strength = 7.25 + 0.697*Hardwood

## Slide 235: Adequacy of the Regression Model

## Slide 236: ANOVA & Regression Analysis
Usually we do ANOVA first then Regression
ANOVA tells us, in general, which factors significantly affect the response
  Often we use the significant factors from ANOVA to build our regression model
Regression analysis tests the significance of a particular model
  There are many regression models which could be fit
    Particularly an issue for multiple linear regression
  If you do not fit a good model, the results could be misleading

## Slide 237: Another example
Does temperature affect concrete density?
If so, how? What is the relationship?
Following data collected in completely randomized order.
Response? Factor? # Factor levels? # Replicates?
Temperature (in degrees) | Density (in lb/ft3) |  |  |  | 
100 | 21.5 | 22.5 | 19.3 | 24.9 | 20.0
125 | 23.0 | 24.8 | 28.4 | 26.4 | 25.5
150 | 30.4 | 28.7 | 29.5 | 30.0 | 25.4
175 | 34.0 | 35.6 | 34.8 | 33.9 | 29.7

## Slide 238: Concrete example
Enter data in Minitab worksheet
  In order collected, if available
Do ANOVA
  Check ANOVA residuals
  Draw conclusions
Do Regression
  Check Regression residuals
  Draw conclusions

## Slide 239: Concrete example
ANOVA Table from Minitab
General Linear Model: density versus temp
Factor Information
Factor Type Levels Values
temp Fixed 4 100, 125, 150, 175
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
temp 3 383.73 127.909 28.27 0.000
Error 16 72.40 4.525
Total 19 456.13
Does temperature affect concrete density?
H0: μ100=μ125=μ150=μ175

## Slide 240: Concrete example: ANOVA Residual Analysis

## Slide 241: Concrete Example
Regression Analysis
Regression Analysis: density versus temp
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 381.421 381.421 91.90 0.000
temp 1 381.421 381.421 91.90 0.000
Error 18 74.705 4.150
Lack-of-Fit 2 2.305 1.152 0.25 0.778
Pure Error 16 72.400 4.525
Total 19 456.125
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.03722 83.62% 82.71% 79.48%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 5.93 2.29 2.59 0.018
temp 0.1562 0.0163 9.59 0.000 1.00
Regression Equation
density = 5.93 + 0.1562 temp
Does temperature affect density? How?
H0:β1 = 0

## Slide 242: Concrete example: Regression Residual Analysis

## Slide 243: More NOTES
Residual analysis from designed experiment will NOT look the same as regression residual analysis
Why? Residuals will not have same values
Remember, in general:
For single factor ANOVA:
For simple linear regression:

## Slide 244: Concrete Example
Predict density at temperature of 160.
Find 90% PI for density at temperature of 160.
Regression Equation
density = 5.93 + 0.1562 temp
Variable Setting
temp 160
Fit SE Fit 90% CI 90% PI
30.9304 0.584791 (29.9163, 31.9445) (27.2551, 34.6057)

## Slide 245: Another Example
How does weight (in lbs) affect time (in sec) to run 100 yards?
Response = Y = ?
Factor = X = ?
Perform ANOVA to determine if weight affects run time?

## Slide 246: ANOVA
General Linear Model: run time versus weight
Factor Information
Factor Type Levels Values
weight Fixed 9 112, 120, 126, 129, 132, 137, 139, 142, 148
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
weight 8 703.6 87.94 * *
Error 0 * *
Total 8 703.6
** Denominator of F-test is zero.

## Slide 247: Plot data in Minitab
Graph
  Scatterplot (simple)
Straight line good fit?

## Slide 248: Find Regression Equation
By Hand or in Minitab
Regression Analysis: run time versus weight
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 1 663.20 663.199 115.03 0.000
weight 1 663.20 663.199 115.03 0.000
Error 7 40.36 5.765
Total 8 703.56
Model Summary
S R-sq R-sq(adj) R-sq(pred)
2.40110 94.26% 93.44% 89.21%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant -81.05 9.94 -8.15 0.000
weight 0.8071 0.0753 10.73 0.000 1.00
Regression Equation
run time = -81.05 + 0.8071 weight
Does weight affect run time?
If so, how?
H0:β1 = 0

## Slide 249: Regression residual analysis

## Slide 250: Predictions
Predict run time for weight of 135 lbs.
run time = -81.1 + 0.807*135 = 27.845 sec
Predict run time for weight of 95 lbs.
run time = -81.1 + 0.807*95 = - 4.44 sec

## Slide 251: Predictions
Predictions only meaningful in general range of original data.
Be very careful extrapolating regression model
Y
X

## Slide 252: Another Example
How does outdoor temperature affect time (in min) to unload truck?
Response = Y = ?
Factor = X = ?
Number of Replicates = ?
Perform ANOVA to determine if temp affects unload time?

## Slide 253: Truck Unload ANOVA
General Linear Model: unload versus temp
Factor Type Levels Values
temp fixed 6 40, 50, 60, 70, 80, 90
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
temp 5 724.28 144.856 20.37 0.000
Error 12 85.33 7.111
Total 17 809.61
Does outdoor temperature affect time (in min) to unload truck?
H0: μ40=μ50=μ60=μ70=μ80=μ90

## Slide 254: Truck Unload Example ANOVA Residual Analysis

## Slide 255: Truck Unload Example
Regression Analysis: unload versus temp
Model Summary
S R-sq R-sq(adj) R-sq(pred)
6.94574 4.66% 0.00% 0.00%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant 36.77 6.44 5.71 0.000
temp 0.0848 0.0959 0.88 0.390 1.00
Regression Equation
unload time = 36.77 + 0.0848 temp
Good regression model for this data? Why?
Does outdoor temperature affect time (in min) to unload truck?

## Slide 256: Truck Unload Example

## Slide 257: Truck Unload Example
Plot data – straight line a good fit?

## Slide 258: Truck Unload Example
Include higher order terms in model e.g. temp2 term
Unload time = β0 + β1temp + β2temp2
Now regression model has more than one term or regressor – called Multiple Linear Regression

## Slide 259: Multiple Linear Regression
General multiple linear regression model with k regressors
Y = β0 + β1X1 + β2X2 + … + βkXk + ε
For our truck unload example
X1 = temp
X2 = temp2
Model a linear function of parameters β0, β1, β2, …, βk
Testing for significance of regression now becomes:
H0: β1 = β2 = … = βk = 0
H1: βk ≠0 for at least one k

## Slide 260: Multiple Linear Regression
Do not add too many terms to model
Adding terms will always make R2 increase
If we had 8 data points, a model with 7 higher order terms will fit perfectly, i.e. R2 = 100%
Y = β0 + β1X + β2X2 + β3X3 + … + β7X7
But too many terms will be difficult to interpret and will not give good predictions
So keep model as low order as possible

## Slide 261: Multiple Linear Regression
For Multiple Linear Regression use Adjusted R2 to measure model adequacy
Adjusted R2 will not automatically increase as terms added to model.
R2 adjusted by the number of terms in model
Where n = # data points and p = # terms in model (including constant)

## Slide 262: Truck Unload Example
Need to include temp2 term in model
Still use Minitab Regression for multiple linear regression
Stat
  Regression
    Regression

## Slide 263: Truck Unload Example
Regression Analysis: unload time versus temp, temp^2
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 2 656.87 328.433 32.25 0.000
temp 1 645.81 645.810 63.42 0.000
temp^2 1 619.15 619.147 60.80 0.000
Error 15 152.75 10.183
Lack-of-Fit 3 67.41 22.471 3.16 0.064
Pure Error 12 85.33 7.111
Total 17 809.61
Model Summary
S R-sq R-sq(adj) R-sq(pred)
3.19108 81.13% 78.62% 72.20%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant -55.7 12.2 -4.56 0.000
temp 3.141 0.394 7.96 0.000 80.22
temp^2 -0.02351 0.00302 -7.80 0.000 80.22
Regression Equation
unload time = -55.7 + 3.141 temp - 0.02351 temp^2
same

## Slide 264: Truck Unload Example
If multiple replicates then error divided into 2 parts:
  Lack-of-Fit: variation due to model inadequacy. If lack-of-fit significant then important terms may be missing from model or model does not explain several large residuals
  Pure Error: random error estimate from multiple replicates
Regression Analysis: unload time versus temp, temp^2
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 2 656.87 328.433 32.25 0.000
temp 1 645.81 645.810 63.42 0.000
temp^2 1 619.15 619.147 60.80 0.000
Error 15 152.75 10.183
Lack-of-Fit 3 67.41 22.471 3.16 0.064
Pure Error 12 85.33 7.111
Total 17 809.61
Model Summary
S R-sq R-sq(adj) R-sq(pred)
3.19108 81.13% 78.62% 72.20%
Summary for regression model (all terms) and error

## Slide 265: Minitab General Regression
Model Summary
S R-sq R-sq(adj) R-sq(pred)
3.19108 81.13% 78.62% 72.20%
R2 (pred) is a measure of how well the model predicts the response.
  R2 (pred) indicates how well the model predicts responses for new observations. Larger values of R2 (pred) suggest models of greater predictive ability. Calculated using the PRESS Statistic.
  PRESS is the sum of squares of the prediction error. In general, the smaller the PRESS value, the better the model's predictive ability. PRESS is used to calculate the predicted R.

## Slide 266: Truck Unload Example
Regression Analysis: unload time versus temp, temp^2
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
Regression 2 656.87 328.433 32.25 0.000
temp 1 645.81 645.810 63.42 0.000
temp^2 1 619.15 619.147 60.80 0.000
Error 15 152.75 10.183
Lack-of-Fit 3 67.41 22.471 3.16 0.064
Pure Error 12 85.33 7.111
Total 17 809.61
Model Summary
S R-sq R-sq(adj) R-sq(pred)
3.19108 81.13% 78.62% 72.20%
Coefficients
Term Coef SE Coef T-Value P-Value VIF
Constant -55.7 12.2 -4.56 0.000
temp 3.141 0.394 7.96 0.000 80.22
temp^2 -0.02351 0.00302 -7.80 0.000 80.22
Regression Equation
unload time = -55.7 + 3.141 temp - 0.02351 temp^2
Model a good fit to data?
Does temperature affect truck unload time?
H0:β1=0
H0:β2=0

## Slide 267: Truck Unload Example Regression Residual Analysis

## Slide 268: Truck Unload Example
Predict unload time for temperature of 55
Unload time = -55.7 + 3.14(55) – 0.0235(552) = 45.94 min
95% PI on unload time for temperature of 55
In Minitab, ‘Prediction’ menu of General Regression Menu

## Slide 269: Truck Unload Example
Regression Equation
unload time = -55.7 + 3.141 temp - 0.02351 temp^2
Variable Setting
temp 55
temp^2 3025
Fit SE Fit 95% CI 95% PI
45.9366 1.04580 (43.7075, 48.1657) (38.7790, 53.0942)

## Slide 270: Regression Analysis
What to do when R2 value not as large as you’d like?
Look at regression residual analysis
  If residual plots look bad
    Try transforming response variable
    Try including higher order term(s) in model
  If residual plots look good
    Indication there are 1 or more significant factors not included in this data
    Rethink experiment

## Slide 271: Choice of Sample Size
A part of any experimental design is to choose sample size
How many replicates to collect at each factor level?
Depends on how large a difference in response means at two factor levels the experimenter defines as statistically different (or the same)?
  Cake baking experiment: if one factor level (# eggs) had a mean cake height of 2” and another factor level had a mean cake height of 3”, is that a significant difference?
  What about 2” vs 2.2”?
In general more replicates needed to detect small effects (i.e. small difference in factor level means); fewer replicates needed to detect large difference in factor level means

## Slide 272: Choice of Sample Size
Blood Coagulation example: conduct an experiment to investigate if diet affects the blood coagulation time (in minutes) of a chemical reaction.
Response: blood coagulation time (min)
Factor: diet
# Factor Levels: 4
We want to be able to detect a difference in the blood coagulation time population means of 5 minutes between any two diets.
We want to reject H0 = μA =μB=μC=μD with probability 90% if the difference in any two factor level means is at least 5 minutes.
D = max difference = 5
Power = 1-β = .90

## Slide 273: Choice of Sample Size
What is Power?
Remember: There are four possible outcomes for a hypothesis test. The outcomes depend on whether the null hypothesis (H0) is true or false and whether you decide to "reject" or “accept" H0.
When H0 is true and you reject it, you make a Type I error. The probability of making a Type I error is called alpha (α) and is sometimes referred to as the level of significance for the test.
When H0 is false and you fail to reject it, you make a type II error. The probability of making a type II error is called beta (β).
 | H0 true | H0 False
Accept H0 | Correct decision p=1-α | Type II error p=β
Reject H0 | Type I error p=α | Correct decision p=1-β
Power

## Slide 274: Choice of Sample Size
The power of a test is the probability of correctly rejecting H0 when it is false. In other words, power is the likelihood that you will identify a significant difference (effect) when one exists.
Ideally, you want to have high power to detect a difference that you care about, and low power for a meaningless difference.
Factors that influence power
  α, the probability of a Type I error (level of significance). As the probability of a Type I error (α) increases, the probability of a type II error (β) decreases. Hence, as α increases, power = 1 - β also increases.
  σ2, the variability in the population. As σ increases, power decreases.
  D, the size of the population difference (effect). As the size of population difference (effect) decreases, power decreases.
  sample size. As sample size increases, power increases.

## Slide 275: Choice of Sample Size
Perform choice of sample size in Minitab
For the blood coagulation example
n = # levels = 4
D = max difference = 5
1-β = power = 0.90
We also need values for σ and α
  σ can be found from ANOVA MSE for pre-experiment or historical data → σ ≈ √MSE
  Remember from ANOVA, MSE = 5.6 → use σ = √5.6 = 2.36643
  Use α = 0.05

## Slide 276: Choice of Sample Size
In Minitab
Stat
  Power and Sample Size
    One-way ANOVA
St. Dev. = √MSE from pre-experiment

## Slide 277: Choice of Sample Size
Power and Sample Size
One-way ANOVA
α = 0.05 Assumed standard deviation = 2.36643
Factors: 1 Number of levels: 4
Maximum Sample Target
Difference Size Power Actual Power
5 8 0.9 0.925940
The sample size is for each level.
n=8 at each factor level
N = 4*8 = 32

## Slide 278: Choice of Sample Size
Now what if we want to detect a difference in factor level means of 3.5 minutes?
  Now D = 3.5 minutes
Will sample size be larger or smaller than when D = 5?
Power and Sample Size
One-way ANOVA
α = 0.05 Assumed standard deviation = 2.36643
Factors: 1 Number of levels: 4
Maximum Sample Target
Difference Size Power Actual Power
3.5 14 0.9 0.900555
The sample size is for each level.
n=14 at each factor level
N = 4*14 = 56

## Slide 279: Choice of Sample Size
Minitab can give sample sizes for several scenarios at once
Enter several detectable differences and/or power values
  Minitab will show sample size for each

## Slide 280: Choice of Sample Size
Power and Sample Size
One-way ANOVA
Alpha = 0.05 Assumed standard deviation = 2.36643
Factors: 1 Number of levels: 4
Maximum Sample Target
Difference Size Power Actual Power
2 32 0.80 0.806766
2 41 0.90 0.902582
2 50 0.95 0.953849
4 9 0.80 0.818083
4 11 0.90 0.901491
4 14 0.95 0.964099
6 5 0.80 0.857319
6 6 0.90 0.930830
6 7 0.95 0.968285
8 4 0.80 0.938456
8 4 0.90 0.938456
8 5 0.95 0.985536
The sample size is for each level.

## Slide 281: Nonparametric Test
ANOVA is a parametric test – based on underlying assumption of normality
What if normality assumption not valid?
  Normal probability plot of residuals really not a straight line
Must use nonparametric test – no assumptions of underlying distributions
Kruskal Wallis – nonparametric equivalent of ANOVA

## Slide 282: Nonparametric Test
Advantages
  Fewer assumptions – valid under weaker assumptions
  Can be used for very small sample sizes
  Can be used for categorical data
Disadvantages
  If distributional assumptions of parametric test are valid, then the parametric test will give a more precise and powerful analysis than nonparametric test

## Slide 283: Kruskal-Wallis Test
Kruskal-Wallis is a test for equality of factor level means; therefore a nonparametric alternative to ANOVA
Kruskal-Wallis is an analysis of variance of ranks
  Each of the N observations replaced by its rank
  Compute average rank for each factor level
  Compare average ranks of the factor levels; if no difference among factor levels then all the average ranks should be approximately equal

## Slide 284: Kruskal-Wallis Test
Rank the observations,Yij, in ascending order
Replace each observation by its rank, Rij, with the smallest observation having rank 1. In the case of ties (i.e. observations with the same value) assign the average rank to each of the tied observations.
Calculate the test statistic, H
where
ni = number of observations in the ith factor level
N = total number of observations
S2 = variance of the ranks (see formula on next slide)

## Slide 285: Kruskal-Wallis Test
If the ni are reasonably large, (ni ≥ 5 ), then H is distributed approximately as χ2α,a-1.
Therefore, if H > χ2α,a-1 the null hypothesis (i.e. all a factor levels produce the same response) is rejected.

## Slide 286: Circuit Noise Example
Example: Does design affect circuit noise?
Response? Factor? # Factor Levels? # Replicates?

## Slide 287: Circuit Noise Example
First try ANOVA
General Linear Model: noise versus design
Factor Information
Factor Type Levels Values
design Fixed 3 1, 2, 3
Analysis of Variance
Source DF Adj SS Adj MS F-Value P-Value
design 2 211.5 105.74 4.77 0.015
Error 32 709.5 22.17
Total 34 921.0
Does design affect circuit noise?
H0: μ1=μ2=μ3

## Slide 288: Circuit Noise Example

## Slide 289: Circuit Noise Example
Regression Analysis: noise versus design
Method
Rows unused 7
Box-Cox transformation
Rounded λ 0
Estimated λ 0.0409679
95% CI for λ (-0.893532, 0.963468)
Regression Equation
ln(noise) = 2.29631 + 0.178536 design
Try Box-Cox transformation in Minitab
ln(noise) = BOXC1
e.g. ln(10.4) = 2.34181

## Slide 290: Circuit Noise Example
Box-Cox transformation in Minitab
  Transform response in >Regression > Regression
  Then use transformed response in ANOVA
  Normal distribution assumption violated – use nonparametric test, Kruskal-Wallis

## Slide 291: Circuit Noise Example
ANOVA residuals do not look good. Normality assumption appears to be violated
Use nonparametric test (Kruskal Wallis) to compare differences in circuit noise among designs

## Slide 292: Circuit Noise Example
Rank the observations,Yij, in ascending order
Replace each observation by its rank, Rij

## Slide 293: Circuit Noise Example
R 1• = 6+7+8+9+10.5+12+13.5+13.5+15+16+17 = 127.5
R 2• = 1+2.5+4+18+19+20+21+22+23.5+23.5+26+31+33+34 = 278.5
R 3• = 2.5+5+10.5+25+27+28+29+30+32+35 = 224
R 1• = 11.59
R 2• = 19.89
R 3• = 22.40

## Slide 294: Circuit Noise Example
For α=0.05
Since 6.629>5.99 we reject H0
We conclude design does affect circuit noise
Table III value

## Slide 295: Circuit Noise Example
In Minitab
Stat
  Nonparametrics
    Kruskal-Wallis
Enter actual responses, not ranks

## Slide 296: Circuit Noise Example
Kruskal-Wallis Test: noise versus design
Kruskal-Wallis Test on noise
design N Median Ave Rank Z
1 11 11.50 11.6 -2.51
2 14 16.25 19.9 0.89
3 10 18.10 22.4 1.61
Overall 35 18.0
H = 6.62 DF = 2 P = 0.036
H = 6.63 DF = 2 P = 0.036 (adjusted for ties)
Does design affect circuit noise?

## Slide 297: HW#3 here
Due date =
Unless otherwise stated, you may use Minitab to do HW assignments
If submitting HW electronically, submit one (1) file only !!!
Can copy Minitab output and paste into MS Word. Use ‘Courier New’ font when pasting Minitab output in MS Word.
Indicate where the answer is located in Minitab output (circle, highlight, etc.)
Data sets can be copied from assignment document and pasted into Excel or Minitab. Some data sets may need to be rearranged before conducting an analysis in Minitab

## Slide 298: Test #1
Test #1 date:
Closed Book
1 page (8.5”x11”) notes. You may write on both sides of the page
Bring a calculator
All relevant statistical tables will be provided
  Z, t, F, χ2, q (tukey test)
No sharing of materials during test
No laptops
No statistical software

## Slide 299: Topics on Test #1
Simple comparative experiments
Single Factor ANOVA
Pairwise comparisons
  CI
  Tukey
Regression Analysis
  Simple Linear
  Multiple Linear
Residual Analysis
  ANOVA
  Regression
Choice of Sample Size
Nonparametric test (Kruskal-Wallis test)
p-value
Covers Chpt.s 1-3; HWs #1, 2, & 3